## Slide 1: To Air is Human…but is it the Best Way to Control IAQ?
William Bahnfleth, PhD, PE
Professor, The Pennsylvania State University
27th Westford Building Science Symposium
August 4-6, 2025

## Slide 2
One of my earliest AIVC memories is a presentation by Andrew Persily where he casually shared his insight that we design our ventilation ‘for no particular reason’. The precise underpinning for many of the requirements included in prescriptive ventilation standards is unclear and this is on purpose. The consensus process from which they originate is a cherished resource to create support and consistent adoption but is not conducive to clear scientific reasoning. An insight that would haunt me ever since.
Jelle Laverge, Ghent University (July 2025)
https://www.aivc.org/sites/default/files/CR22.pdf

## Slide 3: Why ventilate? Conventional wisdom…
Ventilation means dilution with outdoor air
Many air contaminants have indoor sources
  Building materials
  Indoor processes
  Occupants
Consequences of exposure are bad
  Odors
  Chronic toxicity
  Oncogenesis
  Productivity loss
Outdoor air is “fresh” – bring in lots of it to make indoor air fresh, too!

## Slide 4: Dilution
CSS = Steady state concentration of a contaminant
CO = Concentration of contaminant in ventilation air
S = Source strength (emission rate of a contaminant)
Q = Flow rate of uncontaminated ventilation air (e.g., cfm or L/s)

## Slide 5: Dilution has diminishing returns, exponentially growing costs
Suppose ventilation air is contaminant-free (c0 = 0)

## Slide 6: Outdoor air frequently isn’t fresh
“Delhi residents can breathe in ‘moderate’ air quality”

## Slide 7
https://gispub.epa.gov/airnow/

## Slide 8
https://www.iqair.com/in-en/air-quality-map

## Slide 9: Ventilation ≠ outdoor air
Definitions of ventilation in standards:
  (T)he process of supplying air to or removing air from a space for the purpose of controlling air contaminant levels, humidity, or temperature within the space. (ASHRAE Standard 62.1)
  (T)he process of supplying or removing air by natural or mechanical means to or from any space. Such air may or may not have been conditioned. (ASHRAE Standard 62.2)
Related concept - ventilation air:
  (T)hat portion of supply air that is outdoor air plus any recirculated air that has been treated for the purpose of maintaining acceptable IAQ

## Slide 11: Recirculating systems supply outdoor air, filter particles
Outdoor air acts similarly (sort of) on many contaminants
Mechanical filters remove particles – outdoor and indoor sources
Can add other controls for gases and infectious aerosols
Usually, combined effect isn’t quantified

## Slide 12: Recirculation is a mixed blessing
Good
  Higher air change rate clears contaminants faster
  Enables control of indoor contaminant sources with air cleaning
  Air economizer capacity increased
Not so good
  Multiple space recirculation spreads contaminants
  Transport energy increased compared to dual path (DOAS) systems

## Slide 13: Two-Zone Example
Release in Zone 1-Initial concentration of 100%

## Slide 14
Recirculation spreads contaminant to other space, but recirculation through filter speeds up clearance
Notes: This example illustrates the rapidity with which contaminants released in one zone are transported to another zone when there is recirculation. The zones in this case are of identical size, so the maximum concentration in the initially uncontaminated zone is a significant fraction of the initial concentration in the release zone. If this zone had been larger, or there had been additional zones (making the release zone a smaller fraction of the total floor space), the non-release zone peak concentration would have been considerably lower.

## Slide 15: Equivalent clean airflow (ECA) – a better measure of control?
The effect of any control can be expressed in terms of dilution with uncontaminated air
If all controls and removal rates are expressed as ECAs, performance-based IAQ becomes more attainable
Must also rate performance of controls in terms of ECA
If used comprehensively, need at least three types – gas, particle, infectious aerosol

## Slide 16: Equivalent clean airflow of a filter
Dilution Only
Filtration Only
If QV is equivalent clean air for filter, C0  0. can show for a well-mixed space:
Filter has actual airflow Qf and efficiency 

## Slide 17: How much ventilation?
Recommendations have varied widely over two centuries
  Physiological
  Limit infection risk
  Perceived air quality
  Safe contaminant exposures
Stated in terms of outdoor air
Emphasis on energy impact increasing over time
Janssen, J.E., 1999. The history of ventilation and temperature control: The first century of air conditioning. ASHRAE Journal, 41(10), p.48.

## Slide 18: Ventilation is only one way to improve IAQ
Reason, J., 2000. Human error: models and management.
Bmj, 320(7237), pp.768-770.

## Slide 19
2022
2019

## Slide 20: Perception + safety have prevailed for ~100 years in non-healthcare facilities
Acceptable indoor air quality (ASHRAE Standard 62.1): air in which there are no known contaminants at harmful concentrations, as determined by cognizant authorities, and with which a substantial majority (80% or more) of the people exposed do not express dissatisfaction.
1 L/s ≈ 2 cfm

## Slide 21: Current non-residential standards
Ventilation Rate Procedure (VRP, prescriptive)
Per-person rate (Rp) and area rate (Ra)

## Slide 22: Current non-residential standards
Indoor Air Quality Procedure (IAQP, performance)
Design compounds (14 chemicals, 3 mixtures) and PM 2.5
Designer specifies controls – outdoor air, air treatment – to comply with design limits
Must also satisfied perceived air quality requirement
Subjective and objective verification required

## Slide 23
For mixtures, “mixed exposure sum” < 1

## Slide 24: Current residential standards
Same definition of acceptability as 62.1
Similar prescriptive approach
  # Bedrooms ( = people) + area
  Credit for infiltration

## Slide 25: Current residential standards
Recent addenda have addressed
  Use of equivalent clean air approach
  Performance compliance path…but different than 62.1 IAQP
  Control of infectious aerosols by adaptation of ASHRAE Standard 241 requirements (informative appendix)

## Slide 26: Observations on the status quo
We generally know what the rationale is
Quantitative details are hard to come by…if they exist
Ironically, evidence basis is weaker for health care ventilation
Many would like to see the bar raised on what is acceptable
  More transparency regarding basis for requirements
  Performance approach or evidence-based prescriptive
  Expand requirements to new areas – health and productivity
  Bigger role for air cleaning/disinfection – but are we ready to do it?

## Slide 27: Recent research seeks to rationalize IAQ control for chemical and particulate contaminants
Built on work of Logue, et al. (2012)
Objectives
  Quantify and compare harm from indoor air contaminants
  Disability-Adjusted Life-Year basis
Analysis suggests that a small number of contaminants are significant
Environmental Health Perspectives 120:2 CID: https://doi.org/10.1289/ehp.1104035

## Slide 29: Morantes, et al. reexamined residential data
Screened over 300 indoor air contaminants to obtain 25 with useable data
Considered harm (toxicology and epidemiology data)
Quantified harm in DALY per unit of exposure
Applied estimates of typical indoor concentrations
Similar results to Logue, et al.
Proposed basis for an IAQP in ASHRAE Standard 62.2
https://doi.org/10.1021/acs.est.3c07374
Environ. Sci. Technol. 2024, 58, 242−257

## Slide 30: Six contaminants (2 are PM) responsible for 99% of harm – particles pose greatest risk

## Slide 31: Morantes, et al. now extended to offices
Same methodology as in prior residential work
Somewhat different outcome because of differences in contaminant profiles
Particles are still the most harmful
Top four cause > 99% of harm
ASHRAE SSPC 62.1 is considering relevance to IAQP

## Slide 33: DALY may not be the answer to everything, but has a role to play
Trade-offs can be tricky
Calculation of some DALY is not very precise
Work so far has trimmed the list of contaminants of serious concern
Someone still needs to draw the line to define acceptability
Most promising – suggests performance based control may be practical

## Slide 34: New developments – resilience in standards and guidelines: infectious aerosols
Addresses risk of airborne infection transmission in all facility types
Applies during periods of elevated risk (Infection Risk Management Mode, IRMM)
General IAQ standards are prerequisites (e.g., ASHRAE 62.1, 62.2, 170)
Specifies equivalent clean airflow requirements per person (ECAi)
Level playing field for air cleaners
Based on population-level risk assessment, documented in an open publication

## Slide 37: Required ECA depends on space type, number of people and activity
Occupancy categories
  Correctional facilities
  Commercial/retail
  Educational facilities
  Industrial
  Health-care
  Public assembly/sports & entertainment
  Residential
25 space types – office, classroom, food and beverage, etc.
ECAi range 20-90 cfm/pers (10-40 L/s-pers) values doubled if there is loud vocalization
Notes: VECAi= minimum equivalent clean airflow rate required in the breathing zone in IRMM
ECAi=equivalent clean airflow rate required per person in IRMM from Table 5-1.
PZ,IRMM=number of people in the breathing zone in IRMM. Can be different from design occupancy.
Available VECAi and ECAi can determine maximum number of occupants in IRMM.
Current coverage includes 25 space types in 7 occupancy categories, 20-90 cfm/person.

## Slide 38
Table 5-1 – Minimum Equivalent Clean Airflow per Person in Breathing Zone in IRMM

## Slide 39: Comparing standard 62.1 outdoor air, CDC recommendations, and ECAi
ECAi rates are much higher than 62.1 OA rates…but closer after effect of filters is added
Constant risk ECAi values give very different ACH values for different space types
CDC recommends 5 eACH all the time
ECAi has units of flow rate per person because personal risk of infection scales with ECA per person
 | RP [cfm/pers] | RA [cfm/ft2] | Occupant Density [#/1000 ft2]
Office | 5 | 0.06 | 5
Classroom | 10 | 0.12 | 35
Restaurant | 7.5 | 0.18 | 70
ANSI/ASHRAE Standard 62.1 VRP inputs
 | ASHRAE 62.1 Default [cfm/pers] | ASHRAE 241 ECAi [cfm/pers] | ASHRAE 241 ACH with 8’ ceiling
Office | 17 | 30 | 1.1
Classroom | 13 | 40 | 10.5
Restaurant | 10 | 60 | 31.5

## Slide 40: New developments – resilience in standards and guidelines: wildfire smoke
ASHRAE Guideline 44-2024
  Guidance, not code-intended
  Commercial, institutional, health care, multi-unit residential
  Can use for prescriptive or performance-based design
  Focuses on PM control with filters and pressurization
  Addresses operation through development of a Smoke Readiness Plan

## Slide 42: One more layer of complexity – air distribution
All ventilation standards assume “perfect mixing”
Some adjust with factors like ventilation effectiveness
Effectiveness depends on the application
In reality, details of air distribution matter
They are hard to address prescriptively and expensive to address by testing.
Well-mixed space
Mixing ventilation

## Slide 43: Air cleaners are finally getting the attention they need – performance and safety
Covid-driven air cleaner market revealed…
  Most performance claims were unsupported by strong evidence
  Reporting of performance tests was highly misleading
  Safety testing for anything but ozone production
Positive outcome
  Updated and new performance test standards (e.g., ASHRAE 185.3)
  Research on emissions from all air cleaner types
  Byproduct test standard is under development (ASTM WK81750, New Test Method for Chemical Assessment of Air Cleaning Technologies)
https://pubs.acs.org/doi/10.1021

## Slide 44
Link, et al. (2024)
https://doi.org/10.1021/acs.est.3c09331
Environ. Sci. Technol. 2024, 58, 7916−7923

## Slide 45
Outdoor airflow rates
-low 0.3 ACH
-medium 3 ACH
-high 9 ACH
Peng, et al. 2023. doi.org/10.1021/acs.estlett.2c00599
Modeling of byproduct formation – 222 nm and 254 nm GUV, variable outdoor air rates

## Slide 46: Do ventilation units matter?
Air change rates (usually ACH)
  Flow rate measured in room volumes per unit time – not actual replacement
  Used for healthcare, labs, animal facilities
  Expanded use during covid-19 pandemic
  Cannot directly determine contaminant concentration from ACH
  Useful for estimating clearance time, room air distribution
Absolute flow rates (cfm, L/s…) per unit of something
  Per person or per unit of floor area
  Used in residential and non-residential standards
  Needed for calculating concentration

## Slide 47
CSS = Steady state concentration of a contaminant
CO = Concentration of contaminant in ventilation air
S = Source strength (emission rate of a contaminant)
Q = Flow rate of uncontaminated ventilation air (cfm, etc.)
ACR = Air change rate (ACH)
1well-mixed air change reduces concentration by 63%

## Slide 48: ASHRAE sponsored research on evidence for air change rates in standards (1833-RP, 2023)
15 years after publication of Standard 170
“The only robust evidence is that ventilation can be used to control thermal comfort and therefore minimize distraction and fatigue among caregivers.”
“Unfortunately, a single optimal air change rate was not identified for any healthcare space.”
“(G)iven the observed pace of change for the HVAC industry,…air change rate’s days are numbered, but it is likely a large number.

## Slide 49: What about carbon dioxide?
ASHRAE Position Document
  The history CO2 concentrations in relation to building ventilation and IAQ
  Health and cognitive impacts of exposure to CO2
  Existing standards and regulations for indoor CO2 concentrations
  CO2 as an indicator of IAQ and ventilation
  Use of CO2 as a tracer gas for estimating ventilation rates
  Increases in outdoor CO2 concentrations
  Air cleaning directed at CO2 removal alone
  CO2 as an indicator of the risk of airborne disease transmission

## Slide 50: ASHRAE positions, paraphrased
Indoor CO2 concentration is not an overall indicator of IAQ but can be helpful if you know what you’re doing
For the purpose of evaluating ventilation rates, indoor-outdoor CO2 is a tracer gas and is accurate only if inputs are accurate and test assumptions are valid
There is evidence of effects of CO2 at typical indoor concentrationson health, well-being, learning, sleep, and work performance, but it is mixed
In theory, there is a connection between CO2 concentration and airborne infection risk, but in practice, it’s hard to apply
Sensor characteristics and placement are critical for monitoring and control

## Slide 51: ASHRAE Standard 62.1 now supports CO2 Based Demand Control (but I still think it’s a bad idea a lot of the time)

## Slide 52: CO2 Concentration for Steady State 62.1 Compliance Single-Zone, 1000 ft2 Lecture Classroom, 65 Sedentary Adults, 500 ppm Ambient
At full occupancy, 8.4 cfm/pers. Minimum OA 60 cfm

## Slide 53: Wrap-up
Prescriptive outdoor air supply remains the dominant ventilation control for IAQ
Objectives of ventilation standards have not changed much in the past 50 years
There is some evidence behind some outdoor air requirements but not others
There is great interest in improving IAQ, but more outdoor air is not the way to do it

## Slide 54: More wrapping up…
Promising trends
  Standards and guidelines for extreme events
  Equivalent clean air approach
  Performance approach based on quantified harm or benefit/sensor technology to support it
  Evidence that a small (manageable) number of contaminants must be controlled – and PM is #1
  Potential for air cleaners to carry more of the burden – less OA may be fine in some cases
  Improvements in air cleaner testing

## Slide 55: Still wrapping up…
Needs/concerns
  Potential cost and complexity of performance standards
  Some important knowledge gaps
    Air distribution
    Modeling of infection risk
    Air cleaner performance and safety
  Need to harmonize standards
  Need for appropriate level of regulation/enforcement, including post-occupancy

## Slide 56
Thank You!
Bill Bahnfleth
wbahnfleth@psu.edu